## Slide 1
TDMA Schedule Planner and EMANE Integration
Final Technical Presentation | 16-node network | 9-slot heuristic schedule
Part 1
COMPLETE
Part 2
INTEGRATED + VALIDATED
Runtime
16-NEM
TDMA Schedule Planner and EMANE Integration
1

## Slide 2
1. Problem and Design Approach
Centralized TDMA scheduling for one-hop and two-hop interference avoidance
Node coordinates
500 m communication graph
Distance-2 conflict graph
Three greedy colorings
Slot optimization
Slot x Node matrix
Conflict verification
TDMA Schedule Planner and EMANE Integration
2

## Slide 3
2. Part 1 Final Result
Fresh clean execution from sample_input.json
Nodes
16
Range
500 m
1-hop links
42
Conflict links
90
TDMA slots
9
Reused slots
5
Max nodes / slot
4
Verification
PASS
TDMA Schedule Planner and EMANE Integration
3

## Slide 4
3. Node-to-Slot Mapping
The mapping is the interface between the optimizer and EMANE
Node | Slot | Node | Slot | Node | Slot | Node | Slot
Node_01 | 9 | Node_02 | 5 | Node_03 | 6 | Node_04 | 9
Node_05 | 7 | Node_06 | 1 | Node_07 | 2 | Node_08 | 7
Node_09 | 8 | Node_10 | 3 | Node_11 | 4 | Node_12 | 8
Node_13 | 9 | Node_14 | 5 | Node_15 | 6 | Node_16 | 9
TDMA Schedule Planner and EMANE Integration
4

## Slide 5
4. Spatial Reuse and Schedule Matrix
Slot 5: Node_02, Node_14
Slot 6: Node_03, Node_15
Slot 7: Node_05, Node_08
Slot 8: Node_09, Node_12
Slot 9: Node_01, Node_04, Node_13, Node_16
S | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
5 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
6 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
7 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
TDMA Schedule Planner and EMANE Integration
5

## Slide 6
5. Part 2 Integration Architecture
Python schedule is serialized directly into native EMANE TDMA XML
Part 1 optimizer
Node -> Slot
Python bridge
Native EMANE XML
TDMA publisher
16-NEM runtime
Native schedule: 1 ms slot duration | 1 frame | 9 slots | 1 MHz bandwidth | class=0 | 2.4 GHz frequency | 1M datarate
TDMA Schedule Planner and EMANE Integration
6

## Slide 7
6. 16-NEM EMANE Runtime Validation
Clean final publication of the regenerated schedule
Check | Result
NEM 1-16 scheduleAcceptFull | 1 for every NEM
scheduleRejectFrameIndexRange | 0 for every NEM
scheduleRejectOther | 0 for every NEM
scheduleRejectSlotIndexRange | 0 for every NEM
scheduleRejectUpdateBeforeFull | 0 for every NEM
RESULT: the regenerated Python-produced schedule was accepted by all 16 NEMs with zero tested schedule rejections.
TDMA Schedule Planner and EMANE Integration
7

## Slide 8
7. Packet-Level EMANE Test
NEM 1 -> NEM 2 traffic after schedule installation
Test frames generated
50
NEM 2 processedUpstreamPackets
50
NEM 2 numRxSlotValid
64
NEM 2 interface RX packets
64
NEM 2 scheduleAcceptFull
1
NEM 2 scheduleRejectOther
0
Counters are cumulative; the 64 RX/valid-slot value is not interpreted as a 50-packet delivery percentage.
TDMA Schedule Planner and EMANE Integration
8

## Slide 9
8. Tests and Technical Defense
Chain test: two-hop conflict handling - PASS
Spatial reuse test - PASS
500 m boundary test - PASS
16-node final scheduler run - PASS
16-NEM EMANE schedule acceptance - PASS
NEM 1 -> NEM 2 packet path observed
Explain why shortest-path distance <= 2 defines the conflict graph.
Explain communication links versus conflict links.
Explain why greedy coloring is heuristic.
Explain how slot reuse is safe under the conflict graph.
Explain how the Python bridge maps nodes into EMANE slots.
Explain scheduleAcceptFull and scheduleReject statistics.
TDMA Schedule Planner and EMANE Integration
9

## Slide 10
9. Final Status
Part 1: Complete and independently verified
Part 2 bridge: Complete and regenerated from Python
16-NEM runtime: All schedules accepted; zero tested rejects
Packet test: Traffic observed from NEM 1 to NEM 2
Submission package: README + PDF + PPT + source + evidence
TDMA Schedule Planner and EMANE Integration
10