## Slide 1
TDMA Schedule Planner and EMANE Integration
Technical Project Presentation
Candidate: Thamarai Kannan P
Part 1: TDMA Scheduling | Part 2: EMANE Integration
PART 1
16-node TDMA
PART 2
EMANE approach
Technical explanation • documented results • implementation evidence
Notes: Introduce the project in one sentence: first solve the 16-node TDMA scheduling problem, then carry that schedule into EMANE for integration and validation.

## Slide 2
Project Objective
What the project is designed to achieve
01
TDMA Schedule Planner and EMANE Integration
02
Problem
• Allocate TDMA transmission slots to 16 nodes.
• Prevent modeled one-hop and two-hop conflicts.
• Reuse slots where nodes are non-conflicting.
• Carry the final schedule into an EMANE runtime.
Objective
• Build and verify a conflict graph.
• Generate a conflict-free TDMA assignment.
• Convert the mapping into an EMANE TDMA schedule.
• Validate schedule behavior with controlled tests.
INPUT
16-node topology
CORE OUTPUT
9-slot schedule
INTEGRATION
EMANE runtime
Notes: Explain the problem first, then the expected technical flow. Avoid going into implementation details yet.

## Slide 3
Network & Conflict Model
The scheduling constraint is represented as a distance-2 conflict graph
02
TDMA Schedule Planner and EMANE Integration
03
NODES
16
COMMUNICATION RANGE
500 m
DIRECT LINKS
42
DISTANCE-2 CONFLICT LINKS
90
How conflicts are defined
• The network is converted into a conflict graph.
• Conflicting nodes cannot be assigned the same slot.
• Distance-2 modeling includes direct and two-hop conflict relationships.
N
N
N
N
N
Notes: State the documented network values. Then explain why the conflict graph is needed: TDMA slot sharing is decided by conflict relationships, not simply by node identity.

## Slide 4
TDMA Scheduling Approach
From conflict graph to verified slot assignment
03
TDMA Schedule Planner and EMANE Integration
04
1. Build conflict graph
2. Apply graph coloring
3. Generate initial slots
4. Local optimization
5. Verify every conflict
Coloring strategies tested
STRATEGY 1
Largest First (LF)
STRATEGY 2
Smallest Last (SL)
STRATEGY 3
Saturation Largest First (SLF)
SELECTION
Fewest-slot result among tested strategies
The selected coloring is followed by local optimization.
VERIFICATION
Conflict-free assignment
Every edge in the distance-2 conflict graph is checked.
Heuristic result — not a proof of minimum slots
Notes: Explain that graph coloring maps naturally to slot allocation: each color represents a TDMA slot. Mention the three tested strategies, local optimization, and explicit verification. State that the solution is heuristic.

## Slide 5
Final Schedule — Key Results
The verified output of Part 1
04
TDMA Schedule Planner and EMANE Integration
05
Notes: Use the consolidated schedule analysis figure. Point out 16 nodes, 9 slots, 5 reused slots, maximum 4 nodes in one slot, and conflict verification PASS.

## Slide 6
Node-to-Slot Mapping
Exact mapping used for the final schedule
04
TDMA Schedule Planner and EMANE Integration
06
Node | Slot | Node | Slot
Node_01 | 9 | Node_09 | 8
Node_02 | 5 | Node_10 | 3
Node_03 | 6 | Node_11 | 4
Node_04 | 9 | Node_12 | 8
Node_05 | 7 | Node_13 | 9
Node_06 | 1 | Node_14 | 5
Node_07 | 2 | Node_15 | 6
Node_08 | 7 | Node_16 | 9
SCHEDULE
9 slots
REUSE
5 slots
MAXIMUM
Slot 9 → 4 nodes
Notes: Read the exact mapping. Highlight Node_01 = Slot 9 because it is used in the later EMANE enforcement test.

## Slide 7
Spatial Reuse
Why multiple nodes can share the same TDMA slot
04
TDMA Schedule Planner and EMANE Integration
07
Notes: Explain that Slots 5, 6, 7, 8 and 9 are reused. The nodes shown in each group are non-conflicting in the distance-2 graph, so the slot can be reused.

## Slide 8
Python → EMANE Integration
The Part 1 schedule becomes the Part 2 runtime input
05
TDMA Schedule Planner and EMANE Integration
08
01
Node-to-Slot Mapping
→
02
generate_emane_schedule.py
→
03
emane_tdma_schedule.xml
→
04
EMANE Event-TDMA Schedule
→
05
16-NEM Runtime
PYTHON ROLE
Schedule generation + XML conversion
Uses the final Node-to-Slot mapping as the bridge input.
EMANE ROLE
Load schedule + runtime behavior
The generated event-TDMA schedule is loaded into the 16-NEM runtime.
Scheduler output → EMANE schedule → runtime validation
Notes: This is the key Part 2 explanation. The important point is the interface: the Part 1 Node-to-Slot mapping is converted to an EMANE TDMA schedule.

## Slide 9
EMANE Runtime Configuration & Validation
Documented runtime settings and acceptance checks
05
TDMA Schedule Planner and EMANE Integration
09
NEMS
16
SLOT DURATION
1 ms
FRAMES
1
TDMA SLOTS
9
FREQUENCY
2.4 GHz
BANDWIDTH
1 MHz
DATA RATE
1 Mbit/s
SERVICE CLASS
0
SCHEDULEACCEPTFULL
1 for NEMs 1–16
TESTED REJECTION COUNTERS
0
NEM SCHEDULE ACCEPTANCE
16 / 16
RUNTIME RESULT
ACCEPTED
Notes: Explain the configuration values that matter to understanding the test, then state the documented acceptance result: all 16 NEMs accepted the regenerated schedule and tested rejection counters remained zero.

## Slide 10
Packet-Level Enforcement Test
Controlled comparison of allowed and blocked transmission
06
TDMA Schedule Planner and EMANE Integration
10
NODE_01
TDMA Slot 9
→
EMANE INDEX
8 (zero-based)
→
TX TEST
controlled
ALLOWED CASE
50 frames → 17 packets
NEM 1 has a TX opportunity in the corresponding TDMA slot.
BLOCKED CASE
50 frames → 0 packets
The corresponding TX opportunity is removed in a clean run.
ENFORCEMENT RESULT: PASS
Notes: Explain the mapping Node_01 → Slot 9 → EMANE zero-based index 8. Then compare the two clean test cases: allowed gives 17 upstream packets; blocked gives 0.

## Slide 11
Implementation Structure
How the solution is organized in code
07
TDMA Schedule Planner and EMANE Integration
11
SCHEDULING
main.py
End-to-end Part 1 execution
graph_builder.py
Communication and distance-2 conflict graph
coloring.py
Graph-coloring strategies
scheduler.py
Slot numbering and local optimization
verifier.py
Conflict verification
EMANE / VALIDATION
generate_emane_schedule.py
Node-to-Slot → EMANE XML
send_tdma_test.py
Raw Ethernet test
validate_emane.py
Generated XML validation
Part2_Enforcement_Evidence.txt
Allowed / blocked evidence
Notes: Briefly explain the module boundaries. Keep this slide focused on understanding the project structure, not on reading code.

## Slide 12
Conclusion & Technical Takeaways
The complete project story in four points
08
TDMA Schedule Planner and EMANE Integration
12
SCHEDULE
16 nodes → 9 slots
VERIFICATION
Conflict verification → PASS
INTEGRATION
Python mapping → EMANE TDMA schedule
ENFORCEMENT
17 allowed → 0 blocked-case packets
What I should be able to explain
• Why graph coloring is used for TDMA slot assignment
• Why distance-2 conflicts are modeled
• Why the reused-slot nodes do not conflict
• Why 9 slots is a heuristic result, not a proven minimum
What the evidence shows
• The final schedule is verified
• The regenerated schedule was accepted by 16 NEMs
• Tested rejection counters remained zero
• The controlled allowed / blocked test changed packet behavior
Notes: Conclude with the end-to-end story. Be ready to expand verbally on the four technical takeaways and the evidence.

## Slide 13
THANK YOU